## Slide 1: Chapter 9 -- Simplification of Sequential Circuits

## Slide 2: Redundant States in Sequential Circuits
Removal of redundant states is important because
  Cost: the number of memory elements is directly related to the number of states
  Complexity: the more states the circuit contains, the more complex the design and implementation becomes
  Aids failure analysis: diagnostic routines are often predicated on the assumption that no redundant states exist

## Slide 3: Equivalent States
States S1, S2, …, Sj of a completely specified sequential circuit are said to be equivalent if and only if, for every possible input sequence, the same output sequence is produced by the circuit regardless of whether S1, S2, …, Sj is the initial state.
Let Si and Sj be states of a completely specified sequential circuit. Let Sk and Sl be the next states of Si and Sj, respectively for input Ip.
Si and Sj are equivalent if and only if for every possible Ip the following are conditions are satisfied.
  The outputs produced by Si and Sj are the same,
  The next states Sk and Sl are equivalent.

## Slide 4: Equivalent States Illustration
Figure 9.1

## Slide 5: Equivalence Relations
Equivalence relation: let R be a relation on a set S. R is an equivalence relation on S if and only if it is reflexive, symmetric, and transitive. An equivalence relation on a set partitions the set into disjoint equivalence classes.
Example: let S = {A,B,C,D,E,F,G,H} and R = {(A,A),(B,B),(B,H),(C,C),(D,D),(D,E),(E,E),(E,D),(F,F),(G,G),(H,H),
(H,B)}. Then P = (A)(BH)(C)(DE)(F)(G)
Theorem: state equivalence in a sequential circuit is an equivalence relation on the set of states.
Theorem: the equivalence classes defined by the state equivalence of a sequential circuit can be used as the states in an equivalent circuit.

## Slide 6: Methods for Finding Equivalent States
Inspection
Partitioning
Implication Tables

## Slide 7: Finding Equivalent States By Inspection
Figure 9.2

## Slide 8: Finding Equivalent States by Partitioning
Figure 9.3

## Slide 9: Example 9.2 -- Partitioning example
Figure 9.4

## Slide 10: Example 9.3 -- Another partitioning example
Figure 9.5

## Slide 11: Example 9.4 -- Yet another partitioning example
Figure 9.6

## Slide 12: Finding Equivalent States by Implication Tables
Figure 9.7

## Slide 13: Example 9.5 -- Using implication tables to find equivalent states
Figure 9.8

## Slide 14: Example 9.6 -- An implication table example

## Slide 15: Incompletely Specified Circuits
Next states and/or outputs are not specified for all states
Applicable input sequences: an input sequence is applicable to state, Si, of an incompletely specified circuit if and only if when the circuit is in state Si and the input sequence is applied, all next states are specified except for possible the last input of the sequence.
Compatible states: two states Si and Sj are compatible if and only if for each input sequence applicable to both states the same output sequence will be produced when the outputs are specified.
Compatible states: two states Si and Sj are compatible if and only if the following conditions are satisfied for any possible input Ip
  The outputs produced by Si and Sj are the same, when both are specified
  The next states Sk and Sl are compatible, when both are specified.
Incompatible states: two states are said to be incompatible if they are not compatible.

## Slide 16: Compatibility Relations
Compatibility relation: let R be a relation on a set S. R is a compatibility relation on S if and only if it is reflexive and symmetric. A compatibility relation on a set partitions the set into compatibility classes. They are typically not disjoint.
Example: let S = {A,B,C,D,E} and
R = {A,A),(B,B),(C,C),(D,D),(E,E),(A,B),(B,A),(A,C),(C,A), (A,D), (D,A),(A,E),(E,A),(B,D),(D,B),(C,D),(D,C),(C,E),(E,C)}
Then the compatibility classes are (AB)(AC)(AD)(AE)(BD)(CD)(CE)(ABD)(ACD)(ACE)
The incompatibility classes are (BC)(BE)(DE)
Compatible pairs may be found using implication tables
Maximal compatibles may be found using merger diagrams

## Slide 17: Examples 9.8 and 9.9 -- Generating Maximal Compatibles and Incompatibles

## Slide 18: Merger diagrams
Figure 9.11

## Slide 19: Example 9.10 -- Merger diagrams for example 9.8
Figure 9.12

## Slide 20: Minimization Procedure
Select a set of compatibility classes so that the following conditions are satisfied
Completeness: all states of the original machine must be covered
Consistency: the chosen set of compatibility classes must be closed
Minimality: the smallest number of compatibility classes is used

## Slide 21: Bounding the number of states
Let U be the upper bound on the number of states needed in the minimized circuit
Then U = minimum (NSMC, NSOC)
  where NSMC = the number of sets of maximal compatibles
  and NSOC = the number of states in the original circuit
Let L be the lower bound on the number of states needed in the minimized circuit
Then L = maximum(NSMI1, NSMI2,…, NSMIi)
  where NSMIi = the number of states in the ith group of the set of maximal incompatibles of the original circuit.

## Slide 22: State Reduction Algorithm
Step 1 -- find the maximal compatibles
Step 2 -- find the maximal incompatibles
Step 3 -- Find the upper and lower bounds on the number of states needed
Step 4 -- Find a set of compatibility classes that is complete, consistent, and minimal
Step 5 -- Produce the minimum state table

## Slide 23: Example 9.11 -- Reduced state table corresponding to example 9.8
Figure 9.13

## Slide 24: Example 9.12 -- State reduction problem
Figure 9.14

## Slide 25: Example 9.13 -- Another state table reduction problem
Figure 9.15

## Slide 26: Example 9.14 -- Yet another state reduction problem
Figure 9.16

## Slide 27: Example 9.15 -- Optimal state assignments
Figure 9.17

## Slide 28: Unique State Assignments for Four States
Figure 9.18

## Slide 29: State Assignments for a Four State Machine
Figure 9.19

## Slide 30: D flip-flop realization for assignment 1
Figure 9.20

## Slide 31: D flip-flop realization for assignment 2
Figure 9.21

## Slide 32: D flip-flop realization for assignment 3
Figure 9.22

## Slide 33: State adjacencies for four-state assignments
Figure 9.23
Assignment 1
Assignment 2
Assignment 3

## Slide 34: Example 9.18 -- Implication Graphs
Figure 9.24

## Slide 35: Example 9.19 -- Closed subgraphs
Figure 9.24

## Slide 36: Example 9.20 -- Optimal state assignment
Figure 9.26

## Slide 37
Example 9.21 -- Another state assignment problem
Figure 9.27

## Slide 38: A D flip-flop realization of the previous example
Figure 9.28

## Slide 39: Example 9.24 -- Closed partitions
Figure 9.29

## Slide 40: Example 9.25 -- Cross dependency
Figure 9.30